RILEY THEATRE

TECHNICAL SPECIFICATIONS

STAGE DIMENSIONS:

Width- 12.37 metres (1 metre each side is under balcony)

Depth- 9.80 metres (9.00m with cyc or black tabs in))

# Average height to lighting bars - 6.1 metres (4.70m to balcony side bars)

Clearance under balcony- 2.97 metres

STAGE SETTING:

Masking- 5 bays each side (black serge legs at 1.85m, 3.65m, 5.4m, 7.2m and 8.5m from front)

Floor- Grey Harlequin Studio dancefloor (For use with bare feet or agreed footwear only. No stage fixings can be used on the flooring.) A black dancefloor can usually be laid if requested at least one week in advance.

Cyclorama- White pvc projection screen fixed in position. 6.50m high by 10.25 wide.

Full black serge tabs can be drawn in front of the cyc.

LIGHTING TRUSS:

Manufactured by Total Fabrications using heavy duty and medium duty truss with a catwalk at the back of stage (wired for cyc floods) and 7 XO truss flying bars on electric winches. Only one winch may be used at a time. Internally wired lighting bars fixed under first 6 flying bars. Back bar is free for hanging cloths, gauzes etc.

There is no flytower. Height to main truss is 6.92 metres.

Length of bar- 9.80 metres (Foh bar is 5.20 metres)

Vertical load limit per bar- 20 kg per metre

LIGHTING CIRCUITS:

Mains in at 200 amps three phase.

Dimmers- 6 x Strand LD90 digital 24 way. Total 144 10 amp dimmers.

An extra 63 amp three phase outlet (RCCD Ceeform) is available if needed

The theatre has 226 15 amp lighting circuits in total of which 120 are hardwired to dimmers and 106 run to a 24 way IEC patch panel. Circuit distribution:

IWBs-  Foh bar, 12 circuits, 6 hardwired, 6 patchable

Stage bars 1 & 2, 18 circuits, 11 hardwired, 7 patchable

Stage bars 3 to 5, 18 circuits, 10 hardwired, 8 patchable

Overhead circuits total 102, 58 hardwired, 44 patchable

Catwalk- 8 paired circuits hardwired feeding 4 x 4-way 1Kw flood battens

Balcony- 68 circuits, 32 hardwired feeding 8 sidelighting booms, 16 hardwired

feeding 2 balcony crosslighting bars and 6 hardwired foh.14 patchable                                                                                                         (6 each side and 2 foh)

Stage- 34 circuits, all patchable, 28 in groundrow trench, 6 on stage front

Foh- 14 circuits feeding 5 lighting positions under balcony, all patchable.

LIGHTING CONTROL:

ETC Ion with 1 x 20 fader wing and with Net3 remote or iPad virtual RFR

# Strand GeniusPro 520 console (250 channel version) with R120 riggers remote

LANTERNS:

20 x Cantata Fresnel 1.2kw with barndoors

4 x Cadenza Fresnel 2kw with barndoors

12 x Cantata PC 1.2kw  with barndoors

18 x Cantata 18/32 Profile 1.2kw

4 x Cantata 26/44 Profile 1.2 kw

14 x Source Four 50 Profile 575w

16 x Source Four 25/50 zoom profile 750w

12 x Source Four Junior 25/50 575w

4 x CCT Freedom 28/58 Profile 600w

42 x Parcan 1kw (all CP62, some CP61 and CP60 lamps available, call for availability)

24 x Source Four Par 575w with barndoors

12 x Nocturne symmetric flood 1kw

5 x CCT Starlette 4 way flood batten 1kw

SOUND EQUIPMENT:

Players:  2 x Denon DN635 Compact Disc Player

1 x Tascam 801 Minidisc Player/Recorder

Tascam DA-20 Mk II  DAT Player/Recorder

Marantz PMD 321 Compact Disc Player

Playback through QLab on a Mac Mini is available on request.

Laptop playback is also available either through a USB audio DAC or headphone socket.

Microphones: 4 x Shure SM58

2 x Sennheiser G3 series radio handhelds

7 x microphone stands

Mixer:   Digital: Yamaha LS9-16

Analogue: DDA CS3 24 into 4 into 2, 8 stereo line inputs, 16 mic/line inputs

Speakers: 4 x Meyersound UPJ-1P (2 for stalls, 2 for balcony)

2 x Meyersound 500HP Subwoofer

2 x Meyersound UPM1-P (stage monitors)

1 x Meyersound Galileo 480 Loudspeaker Processor

There are 12 send/4 return XLR stageboxes situated downstage left and downstage right running to the control room.

AUDIO VISUAL:

Panasonic PT-EX800 (8000 Lumens) Projector with Standard Lens, 7500 lumens

Hitachi CPX1250 multimedia projector, XGA resolution, 4500 ANSI lumens

BenQ W1070 DLP 1080P Full HD Video Projector, 2000 ANSI Lumens

1 x Wahlberg dmx controlled shutter

COMMUNICATIONS:

Metro Audio system, masterstation in prompt corner, links to LX and sound control, stageright and balcony positions. 4 outstations and 5 headsets.

### GET-IN

There are various routes into the theatre, all of which involve a small set of steps. A disabled lift is available at the main entrance for flightcases but this cannot take large pieces of set. The largest door into the theatre measures 235cm high by 205cm wide.

Compiled by Mark Baker (Technical Manager) mark.baker@nscd.ac.uk

Last updated 18th April 2017

NSCD reserves the right to alter these specifications without notice. Please contact the Technical Manager on 0113 219 3022 for any further information.

#### LIGHTING BAR POSITIONS

(Not to Scale)

Stage: 12.37 wide by 9.8m deep

Distances marked are from stagefront

5 bays per side with fixed flats at 0m, 1.85m, 3.65m, 5.4m, 7.2m and 8.5m

5 sidelighting booms per side at 0.45m, 2.1m, 3.85m, 5.6m and 7.5m

# Height to lighting bars- 6.20 metres (4.70m to balcony side bars)

CYC FLOOD BAR

GROUNDROW

CYC/BLACKS @ 9metres

BAR 6 @ 8.5metres

BAR 5 @ 7.1metres

BAR 4 @ 4.6metres

BAR 3 @ 2.4metres

BAR 2 @ 0metres

BAR 1 @ -3.1metres

# Text boxes

Balcony Side Bar

Balcony Side Bar